## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 7 Physical Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
4G/5G material completely updated; older 2/2.5/3G removed
8.2 (July 2023). Changes from 8.0:
minor updates and additional, including removing master/slave Bluetooth language
expansion, better graphics on wireless link characteristics
expanded, significant revisions of 4G/5G material (but not mobility)

## Slide 2: Physical Layer roadmap
Basic concepts of the physical layer
Basic knowledge of data communication
The transmission medium below the physical layer
Channel multiplexing techniques
Broadband Access Technology

## Slide 3: Basic concepts of the physical layer
The physical layer considers how a stream of data bits can be transmitted over a transmission medium connecting various computers, rather than referring to a specific transmission medium.
The role of the physical layer is to shield the differences between the different transmission media and means of communication as much as possible.
Protocols for the physical layer are also often referred to as physical layer procedures.

## Slide 4: Main tasks of the physical layer
Main task: To determine some features of the interface with the transmission medium.
Mechanical properties: Specify the shape and size of the connectors used for the interface, the number and arrangement of leads, fixing and locking devices, etc.
Electrical characteristics: Indicates the range of voltages present on each line of the interface cable.
Functional characteristics: Indicates the significance of the voltage present at a certain level on a certain line.
Process characteristics: Indicate the order of occurrence of various possible events for different functions.
机械特性：指定用于接口的连接器的形状和尺寸、引线的数量和排列、固定和锁定装置等。
电气特性：表示接口电缆每条线上存在的电压范围。
功能特性：表示某条线路上某一水平电压的显著性。
过程特性：指出不同功能的各种可能事件的发生顺序。

## Slide 5: The model of the data communication system
A data communication system consists of three parts: the source system (or sender), the transmission system (or transmission network) and the destination system (or receiver).
输入数据
发送
的信号(数字的或模拟的)
接收
的信号(数字的或模拟的)
输出数据
源点
终点
发送器
接收器
调制解调器
计算机
调制解调器
数字比特流
数字比特流
模拟信号
模拟信号
输入汉字
显示汉字
目的系统
传输系统
输出信息
计算机
公用电话网
数据通信系统
传输
系统
源系统

## Slide 6: Physical Layer roadmap
Basic concepts of the physical layer
Basic knowledge of data communication
The transmission medium below the physical layer
Channel multiplexing techniques
Broadband Access Technology

## Slide 7: Common terms of Physical Layer
data - The entity that delivers the message.
signal - The electrical or electromagnetic representation of data.
analogous signal - A parameter representing a message whose values are continuous.
digital signal - A parameter representing a message has discrete values.
code - When a digital signal is represented by a waveform in the time domain (or simply the time domain), the basic waveform that represents different discrete values.
数据-传递消息的实体。
信号-数据的电气或电磁表示。
模拟信号-表示值连续的消息的参数。
数字信号-表示消息的参数具有离散值。
码字-当数字信号由时域中的波形表示时，表示不同离散值的基本波形。

## Slide 8: A few basic concepts about channels
Channel - Generally used to refer to a medium that transmits information in a certain direction.
One-way communication (simplex communication) - there can only be communication in one direction and no interaction in the opposite direction.
Bidirectional alternating communication (half-duplex communication) - Both parties can send messages, but they cannot both send (and therefore receive) messages at the same time.
Bidirectional simultaneous communication (full-duplex communication) - Both parties can send and receive information at the same time.
Baseband signal - The signal coming from the source. Data signals such as computer output that represent various text or image files are baseband signals.
Baseband signals often contain more low frequency components, even DC components, but many channels can not transmit this low frequency component or DC component. Therefore, the baseband signal must be modulated.

## Slide 9: A few basic concepts about channels
Modulation is divided into two main categories:
  Baseband modulation: only the waveform of the baseband signal is transformed so that it can be adapted to the channel characteristics. The transformed signal is still a baseband signal. This process is called coding.
  Bandpass modulation: The use of carrier modulation to shift the frequency range of the baseband signal to a higher frequency band and convert it to an analog signal so that it can better transmit over an analog channel (that is, only a range of frequencies can pass through the channel).
  Bandpass signal: A signal modulated by a carrier.

## Slide 10: Common encoding methods
Non-return to zero system: positive level represents 1, negative level represents 0.
Return to zero: Positive pulse represents 1, negative pulse represents 0.
Manchester coding: An up hop at the bit cycle center represents a 0, and a down hop at the bit cycle center represents a 1. But it can also be defined the other way around.
Differential Manchester code: There is always a jump at the center of each bit. Bit-start boundaries with jumps represent 0, while bit-start boundaries without jumps represent 1.
不归零制
曼彻斯特
1
1
1
1
1
0
0
0
0
0
比特流
差分曼彻斯特
归零制
From the signal waveform, it can be seen that Manchester coding and differential Manchester coding produce signals with higher frequency than the non-return-to-zero system.
From the point of view of self-synchronization, the NON-Return-to-zero system cannot extract the signal clock frequency from the signal waveform itself (this is called no self-synchronization ability), while the Manchester code and the differential Manchester code have self-synchronization ability.

## Slide 11: Basic bandpass modulation method
Baseband signals often contain more low frequency components, even DC components, but many channels can not transmit this low frequency component or DC component. To solve this problem, the baseband signal must be modulated.
The most basic binary modulation methods are as follows:
  Amplitude modulation (AM) : The amplitude of the carrier wave varies with the baseband digital signal.
  Frequency modulation (FM) : The frequency of the carrier varies with the baseband digital signal.
  Phase Modulation (PM) : The initial phase of the carrier changes with the baseband digital signal.
0
1
0
0
1
1
1
0
0
AM
FM
PM

## Slide 12: Quadrature Amplitude Modulation
In order to achieve higher information transmission rate, it is necessary to use a technically more complex multi-system amplitude and phase modulation method.
For example:
  There are 1 or 2 amplitudes to choose from. In total, there are 16 combinations, that is, 16 symbols.
  Since there are 16 different combinations of 4 bit codes, each of the 16 points corresponds to a 4 bit code. The data transfer rate can be increased by 4 times.
r

(r, )
Note: The more bits each symbol can represent, the more difficult it is for the receiver to correctly identify each state when demodulation is carried out, and the error rate increases.

## Slide 13: Ultimate capacity of channel
Any practical channel is not ideal, there will be a variety of distortion and interference in the transmission of signals.
The higher the transmission rate of the symbol, the farther the signal transmission distance, or the worse the quality of the transmission media, the more serious the distortion of the waveform at the output of the channel.
实际的信道
（带宽受限、有噪声、干扰和失真）
发送信号波形
接收信号波形
有失真，但可识别
发送信号波形
实际的信道
（带宽受限、有噪声、干扰和失真）
接收信号波形
失真大，无法识别

## Slide 14: Ultimate capacity of channel
Conceptually, there are two factors that limit the transmission rate of a symbol over a channel:
  The range of frequencies through which the channel can pass
  Signal to noise ratio

## Slide 15: The range of frequencies through which the channel can pass
The frequency range that a specific channel can pass through is always limited. Many high-frequency components in the signal often fail to pass through the channel.
In 1924, Nyquist derived the famous Nyquist criterion. He gave an upper bound on the transmission rate of a symbol in order to avoid intersymbol crosstalk under assumed ideal conditions.
  In any channel, the rate of symbol transmission is bounded, otherwise the problem of intersymbol interference will occur, making the decision of symbol (i.e., recognition) impossible at the receiver.
  If the channel has a wider frequency band, that is, the more high-frequency components of the signal can be passed through, then symbols can be transmitted at a higher rate without intersymbol interference.

## Slide 16: SNR (Signal to Noise Ratio)
Noise is present in all electronic devices and communication channels.
The noise is randomly generated and its instantaneous value can sometimes be large. Therefore, the noise will make the receiver make errors in the decision of the symbol.
But the effect of noise is relative. If the signal is relatively strong, then the effect of noise is relatively small.
The SNR is simply the ratio of the average power of the signal to the average power of the noise. It is often written as S/N and is measured in decibels (dB). That is:
SNR= 10 log10(S/N) (dB)
For example, when S/N=10, the SNR is 10dB, while when S/N=1000, the SNR is 30dB.

## Slide 17: SNR (Signal to Noise Ratio)
In 1948, Shannon used the theory of information theory to derive the limit and error-free information transmission rate of the channel with limited bandwidth and Gaussian white noise interference (Shannon formula).
The limiting information transmission rate C of the channel can be expressed as follows.
C = W log2(1+S/N) (bit/s)
Where W is the bandwidth of the channel (in Hz);
S is the average power of the signal transmitted in the channel;
N is the Gaussian noise power inside the channel.

## Slide 18: Shannon's formula shows that
The greater is the bandwidth of the channel or the SNR in the channel, the higher is the limiting transmission rate of information.
As long as the information transmission rate is below the limit information transmission rate of the channel, some way to achieve error-free transmission must be found.
If there is no upper bound on the channel bandwidth W or signal-to-noise ratio S/N (which of course is never the case for real channels), then there is no upper bound on the limit information transmission rate C of the channel.
The achievable information transmission rate over practical channels is much lower than Shannon’s limit transmission rate.
Note: For a defined bandwidth channel, if the signal-to-noise ratio can no longer be improved and the symbol transmission rate has reached the upper bound, there are ways to increase the information transmission rate. That is, using encoding to make each symbol carry more bits of information.

## Slide 19: Physical Layer roadmap
Basic concepts of the physical layer
Basic knowledge of data communication
The transmission medium below the physical layer
Channel multiplexing techniques
Broadband Access Technology

## Slide 20: The transmission medium below the physical layer
The transmission medium, is the physical path between the transmitter and the receiver in the data transmission system.
Transmission media can be divided into two main categories, namely guided transmission media and unguided transmission media.
  In guided transmission media, electromagnetic waves are guided along a solid medium (copper wire or optical fiber).
  Unguided transmission media is free space. In unguided transmission media, the transmission of electromagnetic waves is often referred to as wireless transmission.

## Slide 21: The transmission medium below the physical layer
The spectrum of electromagnetic waves used in telecommunications:
无线电
微波
红外线
可见光
紫外线
X射线

射线
光纤
(Hz)
f
(Hz)
f
LF
MF
HF
VHF
UHF
SHF
EHF
THF
波段
104 105 106 107 108 109 1010 1011 1012 1013 1014 1015 1016
100 102 104 106 108 1010 1012 1014 1016 1018 1020 1022 1024
地面微波
同轴电缆
双绞线
海事
无线电
调幅
无线电
调频
无线电
移动
无线电
卫星
电视

## Slide 22: The transmission medium below the physical layer- Guided transmission media
Twisted pair wire 双绞线
  The most commonly used transmission medium.
  Analog transmission and digital transmission can use twisted pair, the communication distance is generally a few to ten kilometers.
  STP (Shielded Twisted Pair)
  With metal shielding layer
  Unshielded Twisted Pair (UTP)
铜线
聚氯乙烯套层
绝缘层
(a) 无屏蔽双绞线
铜线
聚氯乙烯套层
屏蔽层
绝缘层
(b) 屏蔽双绞线
3 类线
5 类线
(c) 不同的绞合度的双绞线

## Slide 23: The transmission medium below the physical layer- Guided transmission media
In 1991, the Electronic Industries Association and the Telecommunications Industry Association jointly published a standard EIA/TIA-568 for unshielded and shielded twisted-pair cables for indoor data transmission.
The wiring standard was updated to EIA/TIA-568-A in 1995.
This standard specifies five categories of UTP standards (from Class 1 to Class 5).
The most commonly used UTP for transporting data today is Category 5 or CAT5.
绞合线类别 | 带宽 | 线缆特点 | 典型应用
3 | 16 MHz | 2 对 4 芯双绞线 | 模拟电话；曾用于传统以太网 （10 Mbit/s）
4 | 20 MHz | 4 对 8 芯双绞线 | 曾用于令牌局域网
5 | 100 MHz | 与 4 类相比增加了绞合度 | 传输速率不超过100 Mbit/s 的应用
5E (超5类) | 125 MHz | 与 5 类相比衰减更小 | 传输速率不超过 1 Gbit/s 的应用
6 | 250 MHz | 与 5 类相比改善了串扰等性能 | 传输速率高于 1 Gbit/s 的应用
7 | 600 MHz | 使用屏蔽双绞线 | 传输速率高于 10 Gbit/s 的应用
Categories, bandwidths, and typical applications of commonly used stranded wires

## Slide 24: The transmission medium below the physical layer- Guided transmission media
Coaxial cable 同轴电缆
  Coaxial cable has good anti-interference characteristics and is widely used to transmit higher rate data.
  The bandwidth of a coaxial cable depends on the quality of the cable.
  50 Ω coaxial cable - commonly used for LAN/digital transmission
  75 Ω coaxial cable - cable TV/analog transmission commonly used
内导体
外导体屏蔽层
绝缘层
绝缘保护套层

## Slide 25: The transmission medium below the physical layer- Guided transmission media
Optical fiber cable 光纤电缆
  Optical fiber is the transmission medium of optical fiber communication.
  Since the frequency of visible light is very high, on the order of 108 MHz, the transmission bandwidth of an optical fiber communication system is much larger than that of various other transmission media.
高折射率
(纤芯)
低折射率
(包层)
光线在纤芯中传输的方式是不断地全反射
The band of light waves used in optical fiber communications
  The centers of the three commonly used bands are located at 850 nm, 1300 nm and 1550 nm, respectively.
  All these three bands have a bandwidth of 25,000 to 30,000 GHz, which shows that the communication capacity of the fiber is very large.

## Slide 26: The transmission medium below the physical layer- Guided transmission media
Optical fiber advantages
  The communication capacity is very large.
  The transmission loss is small and the relay distance is long.
  Good resistance to lightning and electromagnetic interference.
  No crosstalk interference, good confidentiality.
  Small size and light weight.

## Slide 27: The transmission medium below the physical layer- Unguided transmission media
  The free space is called "unguided transmission medium".
  The frequency band used for wireless transmission is wide.
  Short wave communication (that is, high frequency communication) mainly depends on the reflection of ionosphere, but the communication quality of short wave channel is poor, and the transmission rate is low.
  Microwaves travel mainly in straight lines in space.

## Slide 28: The transmission medium below the physical layer- Unguided transmission media
  In order to use a certain segment of the radio spectrum for communication, it is usually necessary to obtain a license from the relevant radio spectrum management authority of the country‘s government. However, there are also some radio bands that are freely available. For example: ISM (Industrial Scientific Medical). The ISM standards may vary slightly from country to country.
无线局域网使用的 ISM 频段
26 83.5 125
频带 MHz MHz MHz
频率 902 928 2.4 2.4835 5.725 5.850
MHz MHz GHz GHz GHz GHz





## Slide 29: Physical Layer roadmap
Basic concepts of the physical layer
Basic knowledge of data communication
The transmission medium below the physical layer
Channel multiplexing techniques
Broadband Access Technology

## Slide 30: Frequency division multiplexing, time division multiplexing, and statistical time division multiplexing
multiplexing is a fundamental concept in communication technology. It allows users to use a shared channel for communication, reducing cost and improving utilization.
A1
A2
B1
B2
C1
C2
(a) 使用单独的信道
+
( )
+
A1
A2
B1
B2
C1
C2
共享信道
(b) 使用共享信道
复用
分用

## Slide 31: FDM (Frequency Division Multiplexing)
The whole bandwidth is divided into several parts. After a user is allocated a certain frequency band, it will occupy this frequency band from beginning to end in the communication process.
All users of frequency division multiplexing have different bandwidth resources at the same time (note that the "bandwidth" is the frequency bandwidth and not the data sending rate).
频率
时间
频带 1
频带 2

频带 n
频带 3

## Slide 32: TDM (Time Division Multiplexing)
Time division multiplexing divides time into time division multiplexing (TDM) frames of equal length. Each TDM user occupies a fixed sequence number of time slots in each TDM frame.
The slot occupied by each user appears periodically (its period is the length of the TDM frame).
TDM signals are also called isochronous signals.
All users of TDM occupy the same bandwidth at different times.
时间
频率
B
C
D
B
C
D
B
C
D
B
C
D
A
A
A
A
TDM 帧
TDM 帧
TDM 帧
TDM 帧
…
TDM 帧
周期性出现

## Slide 33: TDM (Time Division Multiplexing)
When using time Division multiplexing (TDM) system to transmit computer data, because of the burst nature of computer data, the user's utilization of the assigned subchannels is generally not high.
时分复用可能会造成线路资源的浪费
A
B
C
D
a
b
c
d
t
t
t
t
t
4 个时分复用帧
#1
④
③
②
①
a
c
b
时分复用
#2
#3
#4
用户
当某用户暂时无数据发送时，在时分复用帧中分配给该用户的时隙只能处于空闲状态。
a
b
b
a
d
c
c

## Slide 34: CDM (Code Division Multiplexing)
CDM
  The common term is Code Division Multiple Access (CDMA).
  Each user uses a different code that has been specially selected so that it does not interfere with each other.
  The signal sent by such a system has strong anti-jamming ability, and its spectrum is similar to white noise, which is not easy to be found by the enemy.
Chip Sequence
  Each bit time is divided into m short intervals called chips.
  Each station is assigned a unique sequence of m bit chip slices.
  If bit 1 is sent, its own sequence of m bit chip slices is sent.
  If bit 0 is sent, the binary inverse of the sequence of chip slices is sent.
  For example, the 8-bit chip slice sequence of station S is 00011011.
  When bit 1 is sent, the sequence 00011011 is sent,
  When bit 0 is sent, the sequence 11100100 is sent.
  Chip slice sequence of S station: (-1-1-1 +1 + 1-1 +1 +1)

## Slide 35: CDM (Code Division Multiplexing)
Let vector S denote the slice vector of station S and let T denote the slice vector of any other station.
The sequence of code slices at two different stations is orthogonal, which means that the normalized inner product of vectors S and T is equal to 0:
The normalized inner product of any slice vector and the slice vector itself is one.
The normalized inner product of a vector of code slices and the vector of its inverse is -1.

## Slide 36: CDM (Code Division Multiplexing)
How CDMA works
S 站的码片序列 S
1
1
0
t
t
t
t
t
t
m 个码片
t
S 站发送的信号 Sx
T 站发送的信号 Tx
总的发送信号 Sx + Tx
规格化内积 S  Sx
规格化内积 S  Tx
数据码元比特
发
送
端
接
收
端

## Slide 37: Physical Layer roadmap
Basic concepts of the physical layer
Basic knowledge of data communication
The transmission medium below the physical layer
Channel multiplexing techniques
Broadband Access Technology

## Slide 38: Broadband Access Technology
To connect to the Internet, a user must first connect to an ISP.
In the early days of the Internet, users connected to their ISPs through modems using telephone subscriber lines, which could only access the Internet at a maximum rate of 56 kbit/s.
The FCC used to consider broadband as long as the sum of two-way data rates exceeded 200 kbit/s. But in 2015 it was redefined to:
  Broadband downlink speed reach 25 MBPS
  Broadband uplink speed reach 3 MBPS
From the perspective of broadband access media, it can be divided into two main categories:
  Wired broadband access
  Wireless broadband access

## Slide 39: ADSL 非对称数字用户线路
ADSL (Asymmetric Digital Subscriber Line) technology is to use digital technology to transform the existing analog telephone subscriber line, so that it can carry broadband services.
The frequency band of standard analog telephone signals is limited to 300 to 3400 Hz, but the actual signal frequency that can be passed through the subscriber line itself is still more than 1 MHz.
ADSL technology leaves the 0-4 kHz low-end spectrum for traditional telephone use, and leaves the original unused high-end spectrum for users to use the Internet.
DSL stands for Digital Subscriber Line.

## Slide 40: Several types of ADSL
ADSL stands for Asymmetric Digital Subscriber Line (ADSL)
HDSL (High speed DSL) : High speed digital subscriber line
SDSL (Single-line DSL) : A digital subscriber line with one pair of lines
VDSL (Very high speed DSL) : Very high speed digital subscriber line
DSL (Digital Subscriber Line)
Rate-adaptive DSL (RADSL) : Rate-adaptive DSL, a subset of ADSL that adjusts the line Rate automatically)

## Slide 41: Transmission distance of ADSL
The transmission distance of ADSL depends on the data rate and the diameter of the subscriber line (the thinner the subscriber line, the greater the attenuation of the signal transmission).
The highest data rate that ADSL can achieve is closely related to the signal-to-noise ratio (SNR) at the actual subscriber line.
For example:
  A subscriber line with a diameter of 0.5 mm can travel 5.5 km at a rate of 1.5 to 2.0 Mbit/s, but when the transmission rate is increased to 6.1 Mbit/s, the transmission distance is reduced to 3.7 km.
  If we reduce the diameter of the subscriber wire to 0.4 mm, we can only travel 2.7 km at 6.1 MBPS.

## Slide 42: Features of ADSL
The uplink and downlink bandwidth are made asymmetric.
Uplink refers from the user to the ISP, while downlink refers from the ISP to the user.
ADSL installs an ADSL modem at each end of the subscriber line (copper wire).
In our country, the modulation technique is Discrete Multi-Tone (DMT).
Here "multi-tone" means "multi-carrier" or "multi-subchannel".

## Slide 43: DMT
The DMT modulation technique uses frequency division multiplexing (FDM) method to divide the high end spectrum from 40 kHz to 1.1 MHz into many sub-channels, of which 25 sub-channels are used for the uplink channel and 249 sub-channels are used for the downlink channel.
Each subchannel occupies 4 kHz bandwidth (strictly speaking, 4.3125 kHz) and is digitally modulated using a different carrier (i.e., a different tone). This is equivalent to using many small modems on a pair of subscriber lines to transmit data in parallel.
…
频谱
ADSL 的数字业务
上行信道
传统电话
0
4
下行信道
…
~40
~138
~1100

## Slide 44: Data rate of ADSL
Because the specific conditions of subscriber lines are often very different (distance, wire diameter, interference from adjacent subscriber lines, etc.), ADSL uses adaptive modulation technology to enable subscriber lines to transmit the highest possible data rate.
When ADSL is started, the ADSL modems at both ends of the subscriber line test the available frequencies, the interference in each subchannel, and the quality of the signal transmission at each frequency.
ADSL does not guarantee a fixed data rate. For poor quality subscriber lines can not even open ADSL.
Typically downlink data rates range from 32 kbit/s to 6.4 Mbit/s, while uplink data rates range from 32 kbit/s to 640 kbit/s.

## Slide 45: The composition of ADSL
DSLAM (DSL Access Multiplexer) ：数字用户线接入复用器
ATU (Access Termination Unit) ：接入端接单元
ATU-C (C 代表端局 Central Office)：ATU-R (R 代表远端 Remote)
PS (POTS Splitter) ：电话分离器
基于 ADSL 的接入网的组成
ATU-C
ATU-C
ATU-R
ATU-C
用户线
电话
分离器
至 ISP
居民家庭
基于 ADSL 的接入网
端局或远端站
DSLAM
至本地电话局
PS
PS
区域宽带网

## Slide 46: Second generation ADSL
This includes ADSL2 (G.992.3 and G.992.4) and ADSL2+ (G.992.5).
A higher data rate is obtained by improving the modulation efficiency.
  ADSL2 requires a minimum of 8 MBPS downlink and 800 kbit/s uplink.
  ADSL2+ extends the spectrum range from 1.1 MHz to 2.2 MHz, achieving 16 Mbit/s downlink (maximum transmission rate of 25 Mbit/s) and 800 kbit/s uplink.
Seamless Rate Adaptation (SRA) technology is adopted to adjust the data rate adaptively without interrupting communication and generating bit error.
It improves the line quality evaluation and fault location function, which is of great significance to improve the operation and maintenance level of the network.

## Slide 47: Hybrid Fiber Coaxial Network 混合光纤同轴网络
HFC (Hybrid Fiber Coax) network is a residential broadband access network developed on the basis of CATV, which has a wide coverage at present.
In addition to CATV, HFC network can provide telephone, data and other broadband interactive services.
The existing CATV network is a coaxial cable network with tree topology. It uses frequency division multiplexing of analog technology to transmit TV programs in one direction.

## Slide 48: The backbone of the HFC network uses optical fiber
The HFC network replaces the coaxial cable backbone of the original CATV network with fiber, and uses analog fiber technology.
The amplitude modulation AM of light is used in analog fiber, which is more economical than using digital fiber.
The simulated fiber is connected from the head to the fiber node, which is the Optical Distribution Node (ODN). Optical signals are converted into electrical signals at the fiber nodes. Below the fiber node is the coaxial cable.
同轴电缆
光纤
光纤结点
头端
高带宽光纤
同轴电缆
光纤
HFC 网的结构图

## Slide 49: HFC network has bidirectional transmission function and extends the transmission frequency band
下行信道
上行
信道
5 65 87 1000
调频广播、模拟和数字电视、数据业务
频率(MHz)
我国的 HFC 网的频谱划分

## Slide 50: Cable Modem 调制解调器
Cable modems are modems used for HFC networks.
The most important feature of cable modem is the high transmission rate.
  Downlink rate typically ranges from 3 to 10 Mbit/s, with a maximum of 30 Mbit/s.
  Uplink rate is generally 0.2 to 2 Mbit/s and can reach up to 10 Mbit/s.
Cable modems are much more complex than those used on regular telephone lines, and are not used in pairs but installed only at the user side.

## Slide 51: FTTx
FTTx is a solution to realize broadband residential access network, which represents a variety of broadband fiber access methods.
FTTx stands for Fiber To The... (optical fiber to...) For example:
  FTTH (Fiber To The Home) : Optical fiber is laid all the way to the user's home, which may be the last solution to the residential access network.
  Fiber To The Building (FTTB) : Fiber is converted into electrical signals when it enters the building, and then distributed to users using cables or twisted pairs.